## Slide 1: Module 1 Electronics Circuits
Basic Electronics
BBEE203
Dr. Shalini Hanok
Assistant Professor,
Dept. of ECE,
ATMECE, Mysuru

## Slide 2: RECTIFIERS
A rectifier is a device that converts alternating current (ac) to
direct current (dc).
RECTIFIERS
HALF WAVE RECTIFIERS
FULL WAVE RECTIFIERS
BI-PHASE RECTIFIERS
BRIDGE RECTIFIERS

## Slide 3: HALF WAVE RECTIFIER?
The simplest form of rectifier circuit makes use of a single diode and, since it operates on only either positive or negative half-cycles of the supply, it is known as a half-wave rectifier.
Alternating Voltage
Pulsating DC Voltage

## Slide 4: HALF WAVE RECTIFIER
Semiconductor diodes are commonly used to convert Alternating Current (AC) to Direct Current (DC), also referred as Rectifiers.
The simplest form of rectifier circuit uses a single diode and operates only in positive or negative half cycles of the supply, known as half-wave rectifier.
The mains voltage (220 to 240V) applied to primary of step-down transformer.
The secondary of transformer steps down the 240V rms to 12V rms (the turns ratio 20:1).

## Slide 5: OPERATION OF HALF WAVE RECTIFIER
Diode D1 will allow the current to flow in the direction is shown below.
The Diode D1 will be forward biased during each positive half-cycle and behaves as a closed switch.
When the circuit current flows in opposite direction, the voltage bias across the diode will be reversed, causing the diode to be reverse biased and act like an open switch.

## Slide 6: OPERATION OF HALF WAVE RECTIFIER
T1
RL
Vin
t
-
VL
t
D1 FWD Biased
+
-
Current Flow
+
-
+A
B

## Slide 7: OPERATION OF HALF WAVE RECTIFIER
T1
RL
Vin
t
VL
t
D1 REV Biased
+
-
- A
+ B

## Slide 8: WAVEFORMS OF HALF WAVE RECTIFIER
Vin
t
VL
t
D1 FWD
Biased
D1 REV
Biased
D1 FWD
Biased
D1 REV
Biased
Pulsating Output Voltage

## Slide 9: OPERATION OF HALF WAVE RECTIFIER
The switching action of D1 results in a pulsating output voltage developed
across the load RL.
Since the mains supply is at 50Hz, the pulses of the voltage developed across RL will also be at 50Hz.
During the positive half-cycle, the diode will drop the 0.6 to 0.7V forward threshold voltage normally associated with silicon diodes.

## Slide 10: OPERATION OF HALF WAVE RECTIFIER
However, during the negative half-cycle the peak ac voltage will be dropped across D1 when it is reverse biased.
Assuming that the secondary of T1 provides 12V rms, the peak voltage output from
transformer’s secondary winding will be given by
Vpeak = 1.414 x Vrms = 1.414 x 12V = 16.97V

## Slide 11: OPERATION OF HALF WAVE RECTIFIER
The peak voltage applied to D1 will be approximately 17V.
The negative half cycles are blocked by D1 and thus only positive half cycles appear across RL.
The actual peak voltage across RL will be 17V supplied from secondary of transformer minus the 0.7V forward threshold voltage.
Therefore 16.3V will appear across RL.

## Slide 12: Problem 1
A mains transformer having a turns ratio of 44:1 is connected to a 220 V r.m.s. mains supply. If the secondary output is applied to a half-wave rectifier, determine the peak voltage that will appear across a load.
The r.m.s. secondary voltage will be given by:
The peak voltage developed after rectification will be given by:
Assuming that the diode is a silicon device with a forward voltage drop of 0.6 V, the actual peak voltage dropped across the load will be:

## Slide 13: HALF WAVE RECTIFIER WITH A RESERVOIR CAPACITOR

## Slide 14: HALF WAVE RECTIFIER WITH A RESERVOIR CAPACITOR
Half wave Rectifier with Reservoir
Capacitor
Voltage waveforms at various points in Half-wave Rectifier

## Slide 15: OPERATION OF HALF WAVE RECTIFIER WITH A RESERVOIR CAPACITOR
𝑪𝒉𝒂𝒓𝒈𝒊𝒏𝒈 𝑻𝒊𝒎𝒆 𝑪𝒐𝒏𝒔𝒕𝒂𝒏𝒕 = 𝑺𝒆𝒓𝒊𝒆𝒔 𝒓𝒆𝒔𝒊𝒔𝒕𝒂𝒏𝒄𝒆 × 𝑪𝒂𝒑𝒂𝒄𝒊𝒕𝒂𝒏𝒄𝒆
𝑺𝒆𝒓𝒊𝒆𝒔 𝒓𝒆𝒔𝒊𝒔𝒕𝒂𝒏𝒄𝒆 = 𝑺𝒆𝒄𝒐𝒏𝒅𝒂𝒓𝒚 𝒘𝒊𝒏𝒅𝒊𝒏𝒈 𝒓𝒆𝒔𝒊𝒔𝒕𝒂𝒏𝒄𝒆 + 𝑫𝒊𝒐𝒅𝒆 𝑭𝒐𝒓𝒘𝒂𝒓𝒅 𝒓𝒆𝒔𝒊𝒔𝒕𝒂𝒏𝒄𝒆
RL
Vin T1
t
-
VL
t
D1 FWD Biased
+
-
Current Flow
+
-
+A
B
+
-
Vp
Vp

## Slide 16: Operation of Half Wave Rectifier with a Reservoir Capacitor
-
𝑫𝒊𝒔𝒄𝒉𝒂𝒓𝒈𝒊𝒏𝒈 𝑻𝒊𝒎𝒆 𝑪𝒐𝒏𝒔𝒕𝒂𝒏𝒕 = 𝑳𝒐𝒂𝒅 𝒓𝒆𝒔𝒊𝒔𝒕𝒂𝒏𝒄𝒆 × 𝑪𝒂𝒑𝒂𝒄𝒊𝒕𝒂𝒏𝒄𝒆
T1
RL
Vin
t
VL
t
D1 REV Biased
+
-
+
- A
+
B
+
-
vp
Vp

## Slide 17: Half wave Rectifier with Smoothing Circuit
RC Smoothing Circuit
This circuit employs two additional components, which act as a filter to remove the ripple. The value of additional capacitor is chosen so that the component exhibits a negligible
reactance at the ripple frequency.
The combined effect reduces the
amplitude of ripple, while having
negligible effect on the direct voltage
RC Smoothing Circuit
LC Smoothing Circuit
𝑋𝐶
𝑅2 + 𝑋𝐶 2
LC Smoothing Circuit
At ripple frequency, L exhibits high
inductive reactance while C exhibits a low value of capacitive reactance.

## Slide 18: Problem 2
The R–C smoothing filter in a 50 Hz mains operated half-wave rectifier circuit consists of R1  100ohm and C 2  1,000F. If 1 V of ripple appears at the input of the circuit, determine the amount of ripple appearing at the output.
First we must determine the reactance of the capacitor, C2, at the ripple frequency (50 Hz):
The amount of ripple at the output of the circuit will be given by:

## Slide 19: FULL WAVE RECTIFIERS (FWR)?
Unfortunately, the half-wave rectifier circuit is relatively inefficient as conduction takes place only on alternate half-cycles. A better rectifier arrangement would make use of both positive and negative half- cycles.
Full-wave rectifier circuits offer a considerable improvement over their half-wave counterparts. They are not only more efficient but are significantly less demanding in terms of the reservoir and smoothing components.
There are two basic forms of full wave rectifier; the bi-phase type and the bridge rectifier type.

## Slide 20: BI-PHASE /CENTER TAPPED FWR

## Slide 21: OPERATION OF BI-PHASE RECTIFIER
On the positive half-cycles, point A will be positive with respect to point B. Similarly, point B will be positive with respect to point C.
In this condition D1 will allow conduction (its anode will be positive with respect to its cathode) while D2 will not allow conduction (its anode will be negative with respect to its cathode). Thus, D1 alone conducts on positive half-cycles.

## Slide 22: OPERATION OF BI-PHASE RECTIFIER
On negative half-cycles, point C will be positive with respect to point B. Similarly, point B will be positive with respect to point A. In this condition D2 will allow conduction (its anode will be positive with respect to its cathode). Thus, D2 alone conducts on negative half-cycles.
The result is that current is routed through the load in the same direction on successive half- cycles. Furthermore, this current is derived alternately from the two secondary windings.

## Slide 23: OPERATION OF BI-PHASE RECTIFIER
D1 FWD Biased
T1
+
-
VL
A +
-
B
C
Vin
t
D2 REV Biased
+
RL
-

## Slide 24: OPERATION OF BI-PHASE RECTIFIER
T1
A
+
-
vout
D1 REV Biased
+
-
B
C
vin
t
D2 FWD Biased
+
RL
-

## Slide 25: WAVEFORMS OF BI-PHASE RECTIFIER
Vin
t
VL
t
Pulsating Output Voltage
D1 FWD D2 REV
D2 FWD D1 REV
D1 FWD D2 REV
D2 FWD D1 REV

## Slide 26: OPERATION OF BI-PHASE RECTIFIER
As with the half-wave rectifier, the switching action of the two diodes results in a pulsating output voltage being developed across the load resistor (RL).
However, unlike the half-wave circuit the pulses of voltage developed across RL will occur at a frequency of 100Hz (not 50Hz).
This doubling of ripple frequency allows us to use smaller values of reservoir and smoothing capacitor to obtain the same degree of ripple reduction (reactance of a capacitor is reduced as frequency increases).
As before, the peak voltage produced by each of the secondary windings will be approximately 17V and the peak voltage across RL will be 16.3V (i.e., 17V-0.7V forward threshold voltage dropped by the diodes)

## Slide 27: BI-PHASE FWR WITH RESERVOIR CIRCUIT
The reservoir capacitor C1 can be connected to ensure that the output voltage remains at or near the peak voltage even when the diodes are not conducting.
The capacitor charges to peak value of 16.3V in the positive cycle and holds the voltage at this level when the diodes are non-conducting.
The time required by C1 to charge
to the maximum (peak) level is determined by the
charging circuit time constant (the series resistance
multiplied by capacitance value).

## Slide 28: BI-PHASE FWR WITH RESERVOIR CIRCUIT
The series resistance in this circuit is the secondary winding resistance and forward resistance of the diode and minimal resistance of wiring and the connections.
Hence C1 charges very rapidly as soon as either D1 or D2 starts to conduct.
The time required for C1 to discharge is in contrast, very much larger. The discharge time is equal to product of the capacitance value and RL. In practice, RL is very large and greater than secondary winding, hence capacitor takes longer to discharge.
During this stage D1 and D2 will be reverse biased and held in non-conducting state. As a consequence, the only discharge path for C1 is through RL.

## Slide 29: VOLTAGE WAVEFORMS FOR FULL WAVE RECTIFIER

## Slide 30: BRIDGE RECTIFIER?
An alternative to the use of the bi- phase circuit is that of using a four- diode bridge rectifier in which opposite pairs of diode conduct on alternate half-cycles. This arrangement avoids the need to have two separate secondary windings.

## Slide 31: BRIDGE RECTIFIER

## Slide 32: Operation of Bridge Rectifier
T1
RL
vin
t
vout
D2
D4
B
A +
-
-
+
D1 FWD
FWD
D3 REV
REV
t
-
+

## Slide 33: Operation of Bridge Rectifier
T1
RL
vin
t
vout
A -
B +
FWD D4
D3 FWD
D1 REV
D2 REV
+
-
t

## Slide 34: OPERATION OF BRIDGE RECTIFIER
Avoids 2 separate secondary windings
240V Main voltage is applied to primary of the step-down transformer (T1).
The secondary winding provides 12Vrms of 20:1
On positive half cycles, point A will be positive with respect to B. D1 and D2 will conduct and D3 and D4 will not conduct
On negative half cycles, point B will be positive with respect to A, D3 and D4 will conduct and
D1 and D2 will not conduct.
The current is routed through the load in the same direction on successive half cycles.
Similar to bi-phase rectifier, the switching action of the two diodes results in a pulsating output
voltage being developed across (RL)
The peak voltage is approximately 16.3V (i.e 17V less the 0.7V forward threshold voltage)

## Slide 35: BRIDGE RECTIFIER WITH RESERVOIR CAPACITOR

## Slide 36: Voltage Regulator?
A voltage regulator provides a constant DC output voltage that is independent of AC line voltage variations, load current and temperature.
The input to a voltage regulator comes from the filtered output of a rectifier derived from an AC voltage.

## Slide 37: Voltage Regulator
Rs limits the Zener current to safe limit
The source current is divided as Iz (current through Zener) and IL (current through RL)
It is usual to allow 2-5mA to ensure Zener diode conducts
The output voltage is equal to Zener
breakdown voltage.

## Slide 38: VOLTAGE REGULATOR
The ratio of Rs to RL is significant as the input voltage is voltage divided by them and made available as Vz
𝑉𝑧 = 𝑉𝐼𝑁 𝑋
𝑅𝐿
𝑅𝐿 + 𝑅𝑠
Where VIN is unregulated input voltage
The maximum value of Rs can be calculated from 𝑅
𝑠(𝑚𝑎𝑥) 𝐿
= 𝑅 𝑋
𝑉𝑧
𝑉𝐼𝑁 − 1
The power dissipated in the Zener diode will be given as Pz= Iz X Vz.
The minimum value for Rs is determined from off-load condition –
𝑅𝑠 𝑚𝑖𝑛 =
𝑍
𝑉𝐼𝑁 𝑉𝑍− 𝑉2
𝑃𝑧 max
𝑤ℎ𝑒𝑟𝑒 𝑃𝑧 max is the maximum rated power dissipation for the Zener diode.

## Slide 39: OUTPUT RESISTANCE AND REGULATION
The internal resistance appears at the output of the supply and defined as change in output voltage to change in output current
The regulation is given as

## Slide 40: Problem 3
A 5 V zener diode has a maximum rated power dissipation of 500 mW. If the diode is to be used in a simple regulator circuit to supply a regulated 5 V to a load having a resistance of 400 ohms, determine a suitable value of series resistor for operation in conjunction with a supply of 9 V.
First we should determine the maximum value for the series resistor, RS:
Now we need to determine the minimum value for the series resistor, RS:
Hence a suitable value for RS would be 150 ohms
𝑅
𝑠(𝑚𝑎𝑥)
𝐿
= 𝑅 𝑋
𝑉𝑧
𝑉𝐼𝑁 − 1