## Slide 1
Introduction to the Course
Elements of
Mechanical Engineering
Mr. Anil Kumar K
Assistant professor,
Dept. of Mechanical Engineering,
ATMECE, Mysuru
Elements of Mechanical Engineering
21EME15

## Slide 2
What is Mechanical Engineering?

## Slide 3
Mechanical engineering is the study, design, development, construction, and testing of mechanical and thermal sensors and devices, including tools, engines, and machines. Mechanical engineering careers center on creating technologies to meet a wide range of human needs.

## Slide 4
Mechanical engineering subjects include automobile engineering, manufacturing engineering, power plant engineering, thermal engineering, and mechatronics engineering, which is a combination of electrical, computer, and mechanical engineering.

## Slide 5
MODULE-1
Introduction to Mechanical Engineering

## Slide 6: Role of Mechanical Engineering in Industries and Society:
Product Designer
Core Mechanical Designer/ Machine Designer
Drafts man
Production Engineer
Maintenance Engineer
Quality Engineer
Safety Engineer
PLM Manager
Logistic In-charge
Automation Engineer

## Slide 7
SCOPE OF MECHANICAL ENGINEERING AREAS:
Automobile
Aerospace
Steel Making
Power Plant
Paper Mills

## Slide 8
SCOPE OF MECHANICAL ENGINEERING AREAS:
Chemical Industry
Communication Sector
Railways
ONGC

## Slide 9: Steam
Steam

## Slide 10: Steam
Steam is the gaseous phase of water. It utilizes heat during the process and carries large quantities of heat later. Hence, it could be used as a working substance for heat engines.
Steam is generated in boilers at constant pressure. Generally, steam may be obtained starting from ice or straight away from the water by adding heat to it.

## Slide 11: Application of Steam
In Locomotives
In industries
In power plants
In chemical industries
In paint & dye Industries
In Sugar Industries
In petrochemical Industries
In pharmaceuticals
Food Processing Industries
In Hospitals & Health care Units

## Slide 12: t-h Diagram (Temperature-Enthalpy)
The graphical representation of transformation of 1 kg of ice into 1 kg of superheated steam at constant pressure (temperature vs. enthalpy) is known as t-h diagram.

## Slide 13: Formation of Steam

## Slide 14: Steam

## Slide 15: Important definitions related to Steam
Sensible heat of water (hf ): It is defined as the quantity of heat absorbed by 1 kg of water when it is heated from 0°C (freezing point) to boiling point. It is also called total heat (or enthalpy) of water or liquid heat invariably.
Latent heat or hidden heat (hfg): It is the amount of heat required to convert water at a given temperature and pressure into steam at the same temperature and pressure. It is expressed by the symbol hfg.
Total heat or enthalpy of wet steam (h): It is defined as the quantity of heat required to convert 1 kg of water at 0°C into wet steam at constant pressure. It is the sum of total heat of water and the latent heat and this sum is also called enthalpy.

## Slide 16: Important definitions related to Steam
Superheated steam: When steam is heated after it has become dry and saturated, it is called superheated steam and the process of heating is called superheating. Superheating is always carried out at constant pressure.
Dryness fraction or Quality (x): The term dryness fraction is related with wet steam. It is defined as the ratio of the mass of water vapor in steam to the mass of steam containing it. It is usually expressed by the symbol ‘x’

## Slide 17: Important definitions related to Steam
Enthalpy of liquid:
  hf=Cpw(tf-0)
  Enthalpy of Dry saturated steam:
  hg=hf + hfg
  Enthalpy of Wet steam:
    h=hf + x * hfg
  Enthalpy of Superheted steam:
  hsup= hg + Cps(Tsup –Tsat )

## Slide 18: Steam
Problems on Steam

## Slide 19: Steam tables

## Slide 20: Important definitions related to Steam
Enthalpy of liquid:
  hf=Cpw(tf-0)
  Enthalpy of Dry saturated steam:
  hg=hf + hfg
  Enthalpy of Wet steam:
    hwet=hf + x * hfg
  Enthalpy of Superheated steam:
  hsup= hg + Cps(Tsup –Tsat )
  Specific volume of wet steam
  vwet =x * vg m3/kg
  Specific of Superheated steam:
  vsup= vg x (Tsup /Tsat )

## Slide 21: 1. Find the enthalpy of 1kg of steam at 12 bar when, (a) steam is saturated, (b) steam is 22% wet and (c) superheated to 250oc. Use the steam table. Assume the specific heat of the superheated steam as 2.25 KJ/KgK.
Data:
From the steam tables at 12 bar,
Ts= 188oC
hf=798.43 KJ/kg
hfg= 1984.3 KJ/Kg
Enthalpy of a dry saturated steam:
(b) Enthalpy of wet steam:
(c) Enthalpy of superheated steam:
  h= hf+hfg
  = 798.43+1984.3
  = 2782.73 KJ/Kg
  hwet= hf+x*hfg
  = 798.43+0.78*1984.3
  = 2346.18 KJ/Kg
  hsup= hf+hfg+ Cps(Tsup-Tsat)
  = 798.43+1984.3+2.25(250-188)
  = 2922.23 KJ/Kg

## Slide 22: 2. A steam at 10 bar and dryness 0.98 receives 140KJ/kg at the same pressure. What is the final state of the steam?
Data:
From the steam tables at 10 bar,
Ts= 179.9oC
hf=762.61 KJ/kg
hfg= 2013.6 KJ/Kg
Dryness fraction x=0.98
Enthalpy of wet steam
When 140 KJ of heat is added at the constant pressure its enthalpy will increase
At 10bar the enthalpy of dry saturated steam,
  h= hf+xhfg
  = 762.61+0.98 x 2013.6
  = 2735.9 KJ/Kg
  Enthalpy of heat addition = 2735.9+140
  = 2875.9 KJ/Kg
  hg= hf + hfg
  = 762.61+2013.6
  = 2776.2 KJ/Kg

## Slide 23
Since the enthalpy of steam after heat addition is greater than the enthalpy of dry saturated steam at the same pressure, the steam is superheated.
Then the super heated temperature of the steam is
  hsup= hg+ Cps(Tsup-Tsat)
  2875.9 = 2776.2+2.25(Tsup-179.9)
  Tsup= 224.2 oC

## Slide 24: 3. 6 kg of wet steam contains 0.56kg of water particles in it. What is the dryness fraction of the steam?
Data:
Mass of the water particles = 0.56 Kg
Mass of dry steam preset =
(6-0.56)
  = 5.44/6
  Dryness fraction:
  = 0.906
  = 5.44

## Slide 25: 4. The enthalpy of 1 kg of steam at 70 bar is 2680KJ. What is the condition of the steam?
Data:
From the steam tables at 70 bar,
Ts= 285.8oC
hf=1267.42 KJ/kg
hfg= 1506 KJ/Kg
Hg= 2773.5 KJ/Kg
Since the given enthalpy of the steam is less than the enthalpy of the dry saturated steam at the given pressure, the given steam must be Wet Steam.
Therefore,
  hwet= hf+x*hfg
  = 2680 = 1267.42 + x * 1506
  X= 0.938

## Slide 26: 5. 5 kg of wet steam of dryness fraction 0.8, passes from a boiler to a superheater at a constant pressure of 1MPa absolute. In the superheater the temperature increases to 350oC. Determine the amount of heat supplied in the superheater. The specific heat of super heated steam Cps = 2.25 KJ/KgK
Data: 1MPa= 10bar
From the steam tables at 10 bar,
Ts= 179.9oC
hf=762.6 KJ/Kg
hfg= 2013.6 KJ/Kg
hg= 2776.2 KJ/kg
X = 0.8
hwet= hf+ x * hfg
= 762.6+0.8* 2013.6
= 2373. 48 KJ/Kg
hsup=hg+Cps(Tsup-Tsat)
= 2776.2 + 2.25 (350- 179.9)
= 3158.93 KJ/Kg
Amount of heat supplied = hsup- hwet
= 3158.93-2373.48
= 785.45 KJ/kg
For 5 kg of steam,
= 5 * 785.45
= 3927.25 KJ

## Slide 27: 6. Find the specific volume and enthalpy of 1Kg of steam at 0.8 Mpa. (i) when the dryness fraction is 0.9 (ii) when the steam is superheated to a temperature of 300oC The specific heat of Superheated steam is 2.25kJ/kgK
Data: 1MPa = 10 bar
From the steam tables at 8bar,
Ts= 170.41oC
hf=720.9 KJ/Kg
hfg= 2046.5 KJ/Kg
hg= 2767.5 KJ/kg
hwet=? When x=0.9
hsup = ? When Tsup=300oC
hwet= hf+ x * hfg
= 720.69+0.9* 2046.5
= 2562.54 KJ/Kg
hsup=hg+Cps(Tsup-Tsat)
= 2767.5 + 2.25 (300- 170.41)
= 3059.1 KJ/Kg
vwet =x * vg
= 0.9* 0.2403
= 2.627 m3/kg
  vsup= vg x (Tsup /Tsat )
  = 0.2403()
  = 0.3105 m3/kg

## Slide 28: Application of Steam

## Slide 29
Application of Steam in Sugar Industry:
Stages of Sugar extraction from Sugarcane:
Washing
Extraction
Purifying juice
Crystallization
Centrifugation
Drying

## Slide 30
Application of Steam in Sugar Industry:
Crystallization:
Crystallization is a major process stage that relies on a steam boiler.
In the crystallization process, a vacuum pan evaporates the syrup to saturate with sugar crystals through a process, termed seeding (suspension of Sucrose along with Alcohol and glycerine).
The mixture is further processed in a large container named ‘crystallizer’ to continue crystallization by stirring and cooling the massecuite (mixture of sugar crystal and syrup).

## Slide 31
Application of Steam in Sugar Industry:
Drying:
Large hot air dryers are used to dry damp sugar crystals and reduce their moisture content to as low as 0.02% and then pass it through hot air in a granulator. The dried crystals are later segregated as per their sizes and packed to transfer to the market.

## Slide 32
Application of Steam in Dairy Industry
Steam is quite commonly used for heating and sterilizing dairy equipment, both on the farm and in the dairy manufacturing plant.
The milk processing plants utilize steam for processing and pasteurizing raw milk and dairy products under heat treatment.

## Slide 33
Application of Steam in Paper Industry:
Uniform Heating:
The utilization of rolls in paper processing requires it to be heated internally with steam. Therefore, it is essential to maintain an even temperature across the surface of the rolls for uniformity and high-quality products. Steam is an ideal choice as it condenses and distributes heat evenly.
The saturated steam maintaining the same temperature at a given pressure allows the operators to control the pressure and steam temperature as required.

## Slide 34
Application of Steam in Power Generation:
Steam as motive fluid:
  To Separate and purify process of vapour streams.
  Used for continuous removal of air from surface condensers, in order to maintain desired vacuum pressure on condensing (vacuum) turbines.

## Slide 35
Steam for Atomization
  Atomization refers to breaking the fuels into tiny particles.
  In a steam boiler, atomization takes place in burners. Steam is utilized for atomizing the fuel to ensure a larger surface area that results in effective combustion.
  Atomization also leads to minimal soot formation and acceleration in overall efficiency.

## Slide 36
Steam for Cleaning:

## Slide 37
MODULE-1: Chapter-3
Energy

## Slide 38
What is Energy?
Energy is generally defined as a capacity to do work.
Energy is the primary and most universal measure of all kinds of work by human beings and nature.
According to law of conservation of energy, “Energy can neither be created nor be destroyed but, it can be transformed from one state to another”.

## Slide 39
What are our sources of Energy?
The sources of energy are of two types – non-renewable and renewable.
Non-renewable sources are limited in supply and get depleted by use.
  Oil and coal are examples.
Renewable sources are replenished by natural processes and hence can be used indefinitely.
  Solar, wind, geothermal, ocean energy are examples.

## Slide 40
Non-renewable sources
Fossil fuels are non-renewable energy resources; these are coal, oil and natural gas.
They were formed from the remains of living organisms millions of years ago and they release heat energy when they are burned.
This heat is used to turn water into steam, which is used to turn a turbine, which then drives a generator to generate electricity.
There are downsides however, fossil fuels release Sulphur dioxide and carbon dioxide which lead to acid rain and an increase in global warming.

## Slide 41
Thermal Power plant

## Slide 42
Working of Thermal Power plant

## Slide 43
Advantages:
Less initial cost as compared to other generating stations.
It requires less land as compared to hydro power plant.
The fuel (i.e., coal) is cheaper.
The cost of generation is lesser than that of diesel power plants.
Disadvantages:
It pollutes the atmosphere due to the production of large amount of smoke. This is one of the causes of global warming.
The overall efficiency of a thermal power station is low (less than 30%).

## Slide 44
Nuclear power plant
Nuclear energy is made in power plants by splitting the nuclei of heavy atoms, such as uranium. This splitting of nuclei(nuclear fission)releases a very large amount of energy.
TWO TYPES OF NUCLEAR REACTIONS WHICH RELEASE ENERGY
1. FISSION of the nuclei of some heavy elements
  It is employed in power station and for marine propulsion
  2. FUSION of the nuclei of certain light elements
  Research in the controlled release of thermo- nuclear power from the fusion reaction is being carried out, but so far its only application has been limited to relatively uncontrolled release of power, as in the HYDROGEN BOMB

## Slide 46
Nuclear Fusion Reaction

## Slide 47
Nuclear power plant

## Slide 48
Renewable sources: SOLAR ENERGY
Solar energy is the most readily available source of energy.
Energy extraction using Solar Energy
  Helio-Thermal Process: Flat plate collectors
  Helio-Chemical Process: Photosynthesis
  Helio- Electrical Process: Photovoltaic Conversion

## Slide 49
Helio-Thermal Process: Flat plate collectors

## Slide 50
Helio-Thermal Process: Flat plate collectors

## Slide 51
Helio-Thermal Process: Flat plate collectors

## Slide 52
Helio-Thermal Process: Flat plate collectors

## Slide 53
Helio-Electrical Process: Photovoltaic Systems

## Slide 54
Hydro-electric powerplant

## Slide 55
Shivana Samudra Hydro-electric powerplant

## Slide 56
WIND ENERGY

## Slide 57
WIND ENERGY

## Slide 61: Tidal power plant:
Tide is a periodic rise and fall of the water level of the sea which are carried by the action of the sun and moon on the water of the earth.
The highest level of the tidal water is known as the high tide. The lower level of the water is known as low tide.
The level difference between the high tide and the low tide is known as tidal range.
To set up a tidal power plant, the range should be between 5 meters or more.

## Slide 62: Tidal Cycle:
Lunar Cycle
Day Cycle

## Slide 63: Construction & Working of Tidal power Plant:

## Slide 66
Comparison between Renewable and Non-renewable Energy Resources
Renewable
Non-renewable Energy Resources
These are inexhaustible
Ex:- solar, wind energy etc.
These are exhaustible
Ex:- coal, petroleum, natural gas etc.
Freely available in nature and environment friendly
Not freely available, and also not environment friendly.
They are continuously restored by nature after utilization
These sources once used cannot be recovered any more
Initial cost for utilization of energy sources is high, but maintenance cost is low
Both initial and maintenance costs are high
Availability of energy is intermittent, and hence continuous supply of energy is not possible.
Continuous supply of energy is possible with non-renewable energy sources.

## Slide 67
MODULE-1: Chapter-4
Hydraulic Turbines

## Slide 68
What is a Turbine?
Turbine (Prime mover) is a mechanical device which converts the available kinetic energy from a fluid into mechanical energy.
Ex: Steam turbine, gas turbines, hydraulic turbines etc,.
Depending upon the type of working fluid the turbines are classified into:
1. Steam Turbine
2. Gas Turbines
3. Hydraulic Turbine

## Slide 69
Steam turbine & Gas turbine
Steam Turbine
Gas Turbine

## Slide 71
Hydraulic turbine & its classification
Hydraulic turbine – A rotary engine that converts hydraulic energy into mechanical energy.
Mechanical energy is used in running an electric generator which is coupled to turbine shaft.
The hydraulic Turbines were classified according to the following conditions.
1. Action of water
2. The direction of flow of water
3. Available head
4. Specific speed

## Slide 72
1.Action of water
  Impulse Turbine: There is no pressure drop on the runner/rotor. K.E of water coming from the jet is used to run the runner/rotor.
  Ex: Pelton wheel turbine.
  Reaction Turbine: There is a loss of K.E as well as pressure energy on the runners of the blade.
  Ex: Francis turbine
Hydraulic turbine & its classification

## Slide 73
2.The direction of flow of water:
Tangential: If the water strikes the blades of the runner tangential to the path of rotation called Tangential flow.
  Ex: Pelton wheel turbine.
  Radial: If the water strikes the blades of the runner radially and coming out axially called as Radial flow.
  Ex: Francis turbine
  Axial: In this flow, the water flows parallel to the axis of the turbine.
    Ex: Kaplan turbine
Hydraulic turbine & its classification

## Slide 74
Hydraulic turbine & its classification
3.Available head High head:
High Head: The turbine capable of working under the high potential head of water above 300m
Medium head: The turbine is capable of working under a medium range of potential head about 60m to 300m Ex: Francis turbine.
Low head: The turbine is capable of working under a low range of potential head less than 60m

## Slide 75
4.Specific speed:
Low Specific Speed: Turbine works in the range of 10-50. (Ex: Pelton wheel turbine)
Medium Specific Speed: Turbine works in the range of 50-350. (Ex: Francis turbine)
High Specific Speed: Turbine works in the range of 250-850. (Ex: Kaplan turbine)
Hydraulic turbine & its classification

## Slide 76
PELTON WHEEL

## Slide 77
Reaction TURBINE: Francis turbine

## Slide 78
Reaction TURBINE: Kaplan turbine

## Slide 79
Turbine comparison
Impulse Turbine | Reaction Turbine
The entire energy of the water is first converted into kinetic energy. | The available energy of the water is not converted from one from to another. (partial reduction of pressure and velocity)
The water flows through the nozzles and impinges on the buckets, which are fixed to the outer periphery of the wheel | The water is guided by the glide blades to flow over the moving vanes.
The water impinges on the buckets with KE | The water glides over the moving vanes with PE
The pressure of the flowing water remains unchanged and is equal to the atmospheric pressure | The pressure of the flowing water reduced after gliding over the vane.
It is not essential that the wheel should run full | It is essential that the wheel should always run full and kept full of water
It is possible to regulate the flow without loss | It is not possible to regulate the flow without loss
Impulse turbine has more hydraulic efficiency | Reaction turbine has relatively less efficiency
Impulse turbines operates at high water heads | Reaction turbines operates at low and medium heads
Example of impulse turbine is Pelton wheel | Example of reaction turbine are Francis turbine, Kaplan and propeller turbine.

## Slide 80
Pelton wheel

## Slide 81
Francis turbine

## Slide 82
Kaplan turbine

## Slide 83: What is a pump?
A hydraulic pump is a mechanical device of power that converts mechanical power into hydraulic energy.
Hydraulic pumps are used to lift the water from low head to high head.
When a hydraulic pump operates, it creates a vacuum at the pump inlet, which forces liquid from the reservoir into the inlet line to the pump and by mechanical action delivers this liquid to the pump outlet and forces it into the hydraulic system.

## Slide 84: Classification of Hydraulic pumps
Water
Pumps
Dynamic pressure Pumps
Positive Displacement Pump
Centrifugal Pump
Jet Pump
Reciprocating Pump
Piston Plunger Pump
Rotary Pump
Diaphragm Pump
Gear Pump
Lobe Pump
Vane pump

## Slide 85: Centrifugal pump
It uses rotational kinetic energy to deliver the fluid.
The rotational energy typically comes from an engine or electric motor.
The fluid enters the pump impeller along or near to the rotating axis, accelerates in the propeller and flung out to the periphery by centrifugal force
In centrifugal pump the delivery is not constant and varies according to the outlet pressure.
These pumps are not suitable for high pressure applications and are generally used for low-pressure and high-volume flow applications.
The maximum pressure capacity is limited to 20-30 bars and the specific speed ranges from 500 to 10000.

## Slide 86
Thank You
Mr. Anil Kumar
Assistant professor,
Dept. of Mechanical Engineering,
ATMECE, Mysuru